## Slide 1
SMART-ROOM TOXIN PURIFIER
Real-Time Analysis of 3D Diffusion Fields
Multivariable Calculus & Control Systems Engineering
Authors: KEBBANE Ouael, BENDILMI Mélissa, ALLALOU Lilia Assia, FERHAT Abdeldjalil Nassim

## Slide 2
PROJECT OVERVIEW
⚠️
THE PROBLEM
Toxic fumes diffuse through a 3D room. We need real-time control to keep air safe.
🔬
THE SOLUTION
Smart purifier regulated by PID controller, computing 3D concentration field in real-time.
∑
THE MATH
3D diffusion PDE + triple integration + Laplace-domain control theory.

## Slide 3
MATHEMATICAL FOUNDATION: 3D DIFFUSION
The Diffusion Equation (PDE)
∂C/∂t = D(∂²C/∂x² + ∂²C/∂y² + ∂²C/∂z²)
Where:
• C = toxin concentration
• t = time
• D = diffusion coefficient
• ∇² = Laplacian (3D)
Shows how toxin spreads through space over time.
Finite Difference Method
Grid-based discretization:
7×5×7 = 245 cells
Each cell stores concentration
Laplacian calculated using 6 neighbors
Advantages:
✓ Fast computation with NumPy
✓ Captures spatial variations
✓ Real-time updates
✓ Easy to visualize

## Slide 4
TRIPLE INTEGRATION: TOTAL TOXIN MASS
T(t) = ∭ᵥ C(x,y,z,t) dV
1
Sum All Concentrations
Add up toxin levels from all 245 grid cells
2
Scale by Cell Volume
Multiply by dV (volume of each cell) to get total mass
3
Real-Time Feedback
Use this value to control the purifier fan speed

## Slide 5
CONTROL THEORY: LAPLACE-DOMAIN PID
Transfer Function: H(s) = Kp + Ki/s + Kd·N·s/(s+N)
P
Proportional
Kp × error
Immediate reaction to current toxin level
I
Integral
Ki ∫ error dt
Corrects accumulated errors over time
D
Derivative
Kd × d(error)/dt
Anticipates future changes in toxin level

## Slide 6
TUSTIN (BILINEAR) TRANSFORM
Continuous Time (s-domain)
Classical calculus with continuous differential equations.
Ideal for theory, but computers work in discrete time steps.
s ≈ (2/dt) × (z-1)/(z+1)
where z is the shift operator (one time step back)
Discrete Time (z-domain)
Simulations run at fixed time steps (dt = 30 ms). The Tustin transform bridges theory and practice.
I[n] = I[n-1] + (dt/2)×(e[n]+e[n-1])
Simple recursive arithmetic executed by Python at each time step.

## Slide 7
SYSTEM ARCHITECTURE
Toxin Sources
(Leaks)
3D Concentration
Field C(x,y,z,t)
Triple
Integration
PID Controller
u(t)
🌪️ PURIFIER UNIT (Sink) — Suction proportional to u(t)
Feedback Loop
Current toxin mass T(t) is measured and fed back to the controller, which adjusts fan speed in real-time to maintain air safety.
Key Metrics Tracked in Real-Time:
• Total toxin mass T(t) • Peak concentration C_max • Fan speed output u(t) • Leak detection

## Slide 8
VISUALIZATION & REAL-TIME PERFORMANCE
3D Vector Field & Voxels
✓ Color-coded toxin concentration
✓ Flow field arrows show suction paths
✓ Voxel spheres expand with danger
✓ Real-time particle smoke trails
Live Performance Graphs
✓ Red line: Total toxin mass T(t)
✓ Cyan line: Fan speed u(t)
✓ Orange line: Peak concentration
✓ 60-second rolling history
⚡ Performance Optimizations
50× speedup using NumPy vectorization • Precomputed Gaussian masks • Efficient Laplacian computation • 33 physics updates per real second (dt=30ms)

## Slide 9
IMPLEMENTATION DETAILS
GRID PARAMETERS
NX × NY × NZ: 7×5×7
Total cells: 245
dx: 1.71 m
dy: 1.6 m
dz: 1.71 m
dV: 4.41 m³
D: 0.35 m²/s
PID PARAMETERS
Kp: 3.8
Ki: 0.05
Kd: 2.0
N (filter): 20.0
dt: 30 ms
I_CLAMP: ±60
SIMULATION
Framework:
VPython
Libraries:
NumPy
Matplotlib
KEY FEATURES & INTERACTIVITY
• Up to 3 simultaneous leaks active at once
• Shock-wave rings on leak detection
• Live Kp/Ki/Kd slider adjustment during simulation
• Anti-windup integrator clamping to prevent controller saturation
• Color-coded danger levels: Green (safe) → Yellow (warning) → Red (critical)
• Particle smoke trails showing toxin advection toward purifier

## Slide 10
RESULTS & DATA ANALYSIS
✓ SCENARIO 1: Safe State
Initial state before any leak. Room fully clean, T(t) ≈ 0, fan off.
Status: AIR QUALITY 100% SAFE
Display: Green room, safe indicators
⚠️ SCENARIO 2: Active Leak
Toxin diffuses from leak source. T(t) rises, controller ramps fan speed.
T(t) = 1758.69 (from triple integral)
Display: Orange room, flashing danger, max concentration shown
CONTROLLER RESPONSE IN REAL-TIME
1.
Error Detected
T(t) rises above safe threshold. e(t) = T(t) > 0
2.
PID Computes
P: immediate response | I: accumulates error | D: predicts trend
3.
Fan Activates
u(t) increases smoothly, proportional to toxin load
4.
Purification
Sink term grows with fan speed; toxin decreases until safe

## Slide 11
PROJECT SUMMARY
Bridging Theory & Practice
✓ Implemented 3D PDE solver using finite differences + NumPy vectorization
✓ Computed triple integrals in real-time for feedback control
✓ Designed & discretized Laplace-domain PID using Tustin transform
✓ Created interactive 3D visualization with live performance graphs
✓ Achieved 50× speedup through mathematical optimization
TECHNOLOGIES:
Python • NumPy • VPython • Matplotlib • Calculus • Control Theory • Signal Processing

## Slide 12
THANK YOU
Smart-Room Toxin Purifier
Authors: KEBBANE Ouael • BENDILMI Mélissa • ALLALOU Lilia Assia • FERHAT Abdeldjalil Nassim